8182 Connectors

P1/P2- IDC 10 pin bump polarized.

| Pin | P1-RTU | P2-PC |
| --- | --- | --- |
| 1 | +12Vdc* | CD |
| 2 | N/C | RxD |
| 3 | RxD | TxD |
| 4 | N/C | DTR |
| 5 | CTS | SG |
| 6 | RTS | DSR |
| 7 | SG | RTS |
| 8 | TxD | CTS |
| 9 | CD | RI |
| 10 | -12Vdc* | N/C |

* Current limited to 20mA

TB1- Fixed screw cage-clamp terminal strip or RJ45.

| Pin | RJ45* | Terminal Block |
| --- | --- | --- |
| 1 | Earth | PTT+ |
| 2 | PTT+ | PTT- |
| 3 | RxA+ | Common |
| 4 | TxA+ | Earth |
| 5 | TxA- | RxA- |
| 6 | RxA- | RxA+ |
| 7 | PTT- | TxA- |
| 8 | Common | TxA+ |

* Conforms to MODEM standards.

.

JP1- External Power Header.

| Pin | Description |
| --- | --- |
| 1 | +12Vdc |
| 2 | N/C |
| 3 | GND |
| 4 | N/C |
| 5 | -12Vdc |

2/4 Wire Mode Operations

2 Wire Mode:

- Jumper E1, pin 1-2 shorted.

- Connector TB1 (Terminal Block)

Pin 7 PTT-

Pin 8 Common

4 Wire Mode:

- Jumper E1, pin 2-3 shorted.

- Connector TB1 (Terminal Block)

Pin 5 TxA-

Pin 6 RxA-

Pin 7 PTT-

Pin 8 Common

Jumper Settings

Jumper settings in Bold-face type are factory settings.

| Jumper | Setting | Function |
| --- | --- | --- |
| E1 | 1-2 | Two wire modem communications |
|  | 2-3 | Four wire modem communications |
| E2 | 1-2 | Bell202 |
|  | Parked | CCITT v.23 |
| E3 | 1-2 | Modem in CCITT v.23 mode |
|  | 2-3 | Modem in Bell202 mode |
| E4 | 1-2 | Key Carrier |
|  | Parked | No key carrier |