Description

The RTU8195 Bell202 modem provides the Siemens S5-95U PLC compatibility with a variety of SCADA and Host CPU systems via radio, leaseline, audio or general EIA232 interfaces.

Following Materials are supplied with the RTU8195 package:

- RTU8195 Bell202 Modem.

- The CDR1512 cable to connect the 8195 to the S5-95U PLC.

- S5-95U EPROM w/ Modbus Protocol.

- IBM-PC Configuration/Demonstration Software on a 3.5" diskette.

The user will supply the following materials.

- Siemens S5-95U PLC.

- IBM or compatible PC with 3.5" floppy drive.

- A cable connecting the RTU8195 to the appropriate media.

- An available COM1: port on the PC.

Jumper Settings

E1- Two wire/ four wire communications

  - Two wire communications

(Factory Setting).

  - Four wire communications

Adjustments

R22- Transmitter Gain

- Place a 600 Ohm load across TxA- and TxA+.

- Short jumper E4.

- Measure at output.

- Adjust output.

Transmitter gain is adjustable from -20 dB to -3 dB +/- 5%. The factory setting is -9 dB.

RTU8195 Keygen Installation

Connectors and wiring

There a two connections on the RTU8195, J1 is the S5-95U port and J3 is the modem port. Table 1 shows the pinouts of these two connectors.

Table 1 RTU8195 J1 and J3 Pin-outs

| J1 PLC | J3 Line |
| --- | --- |
| Pin | Desc | Pin | Desc |
| 1 | +5 Vdc | 1 | Earth |
| 2 | TTY In- | 2 | PTT+ |
| 3 | TTY Out- | 3 | RxA+ |
| 4 | Mext | 4 | TxA+ |
| 5 | Mext | 5 | TxA- |
| 6 | M | 6 | RxA- |
|  |  | 7 | PTT- |
|  |  | 8 | Common |

The RTU8195 connects to the S5-95U via the CDR1512 Cable. Insert the modular phone plug side of the cable into the PLC port of the RTU8195. Connect the other side of the cable to the communication port of the S5-95U. Next, insert the EPROM module into the EPROM slot on the S5-95U. Connect a cable between the RTU8195 and appropriate media.

# Figure 2 RTU8195 Installation

Software Installation and Start-up

The configuration/demonstration software may be installed on the hard drive or may run from the floppy drive. To install the software on your hard drive follow the directions below.

Hard Disk Installation

- Insert the 3.5" floppy containing software into drive A.

- Type “a:\install a: c:” to install the software.

- After the installation type “cd c:\MODRTU” to select the software directory.

- Type “MODRTU” to run the software program.

- Type the number of the RTU when prompted and press [Return]. default setting is 1.

- The software will search for the RTU.

- Once the RTU is found the RTU type and baud rate will display in the lower right hand corner.

S5-95U Start-up

The following procedure provides the information required to load the Modbus protocol into the S5-95U internal memory and start up the S5-95U.

Remove the battery From the 95U. Set run switch in the “STOP” position. If the unit is already powered remove the power and wait 30 seconds. Install EPROM containing Modbus protocol. Re-apply power to the 95U, otherwise turn on the 95U. The Modbus protocol is now loaded into the 95U internal memory. Re-install the battery, then cycle the power to the 95U. Set the run switch to “RUN”. The 95U is now ready to communicate under its default settings.

Figure 3 S5-95U Labeling

Modbus Addressing

Table 2 Standard Modbus Addressing

| Outputs | Inputs | Analogs |
| --- | --- | --- |
| Mod bus | S5 | Mod bus | S5 | Mod bus | S5 |
| 257 | Q32.0 | 10,256 | I32.0 | 40011 | AI1 |
| 258 | Q32.1 | 10,257 | I32.1 | 40012 | AI2 |
| 259 | Q32.2 | 10,258 | I32.2 | 40013 | AI3 |
| 260 | Q32.3 | 10,259 | I32.3 | 40014 | AI4 |
| 261 | Q32.4 | 10,260 | I32.4 | 40015 | AI5 |
| 262 | Q32.5 | 10,261 | I32.5 | 40016 | AI6 |
| 263 | Q32.6 | 10,262 | I32.6 | 40017 | AI7 |
| 264 | Q32.7 | 10,263 | I32.7 | 40018 | AI8 |
| 265 | Q33.0 | 10,264 | I33.0 | 40019 | AQ1 |
| 266 | Q33.1 | 10,265 | I33.1 |  |  |
| 267 | Q33.2 | 10,266 | I33.2 |  |  |
| 268 | Q33.3 | 10,267 | I33.3 |  |  |
| 269 | Q33.4 | 10,268 | I33.4 |  |  |
| 270 | Q33.5 | 10,269 | I33.5 |  |  |
| 271 | Q33.6 | 10,270 | I33.6 |  |  |
| 272 | Q33.7 | 10,271 | I33.7 |  |  |

Table 3 S5-95U Packed I/O Addressing

| Packed I/O |
| --- |
| Modbus | S5 | DB253 DW |
| 40001 | Status | 0 |
| 40002 | IW32 | 1 |
| 40003 | QW32 | 2 |
| 40004 | IW34 | 3 |
| 40005 | CTR0 | 4 |
| 40006 | CTR1 | 5 |
| 40007 | CTR2 | 6 |
| 40008 | CTR3 | 7 |
| 40009 | IW36 | 8 |
| 40010 | IW38 | 9 |
| 40011 | AI1 | 10 |
| 40012 | AI2 | 11 |
| 40013 | AI3 | 12 |
| 40014 | AI4 | 13 |
| 40015 | AI5 | 14 |
| 40016 | AI6 | 15 |
| 40017 | AI7 | 16 |
| 40018 | AI8 | 17 |
| 40019 | AQ1 | 18 |

Siemens Step-5 Support

Note: The Modbus Host test software is intended for demonstration and system integrity use, not as a  SCADA host. This software will allow polling of up to 4 95RTU’s on com port 1. The polled data

from the RTU will be displayed in binary for status, decimal for counters, and 0-1000 engineering unit for analog value format on the screen.

The user should have a working knowledge of Siemens Step 5 and Step 6 Software. Contact your local Siemens distributor for support and training.

DB253 is the user definable Data Block. This area in the PLC is only accessible though the S5 programming port using Siemens software.

Caution: DB, FB and FW 200 and above can not be used. All user programs should be called from PB 1.

Table 4 Step-5 Support.

| Function | Data Word | Default |
| --- | --- | --- |
| Station Number* | DW 129 | 1 |
| Baud Rate** | DW 157 | 1200 baud |

* The RTU Station Number range is from 1 to 254 decimal.

** Baud Rates supported for the RTU8191 are 300, 600, 1200, 2400, 4800, 9600.

Quick Start

This procedure will provide you with step by step instructions on polling the PLC with function code 3: Read Holding Registers. The keygen must be configured for EIA232 DCE (see the jumper settings section in this documentation). This procedure will verify that the PLC is communicating.

- If you have already installed the software on to your hard drive type “MODRTU”, if not insert the software disk into the floppy drive, access the drive and type “MODRTU”.

- Enter a “1” at the RTU number prompt. The software will then search for the PLC and connect at the appropriate baud rate. Once connected the software will display “baud xxxx 95RTU” in the lower right corner.

- From the main menu press [F1].

- At the function window press [F3]for Read Holding Registers.

- POLL NUMBER ? 				Type “1" press [Return].

- RTU NUMBER ? 				Type “1" press [Return].

- STARTING HOLDING REGISTER ? 			Type “1" press [Return].

- NUMBER OF HOLDING REGISTERS TO READ? 					Type “19" press [Return].

- Press [F2] to poll and display the data. The holding register response window will then display.

We have now verified that the PLC is communicating through the RTU8191.

User Programs

User programs are called form PB1. Use the hook-up to an IBM-PC for testing user programs. After programs are tested modem’s or radios can be installed.

All trademarks acknowledged.

Polybus International is not responsible for any errors or omissions in this documentation.

Polybus International reserves the right to change specifications without notice.

Polybus International, Inc.

1258-H Quarry Lane

Pleasanton, CA 94566

P- 510.426.4815

F- 510.484-5469

Web- http://www.rtu.com